## Slide 1: Differential Non-Linearity in BNL Chevron Data

## Slide 2: Origin of DNL for Chevrons
DNL arises from the fact that there is an offset between the calculated centroid and the true hit position. In our case, we assume the centroid is linearly proportional to the charge on the pads, but depending on how the charge actually couples to the pads, this may not be so, in particular for a somewhat complicated structure like a chevron.
For the FNAL chevron beam test data, the charge footprints at smaller angles are of the order of the size of the pad spacing (or effective pad area), and the charge has a tendency for being distributed more or less equally between two pads or symmetrically around 1 pad. The calculated centroid then is either peaked at a position between the center of adjacent pads, (ie, at the nominal pad edge), or at the pad center.
As shown in the following slides, this tendency for the centroid to peak at the pad center and at the pad edge is why there is a differential non-linearity (DNL) present in our data. That is, the charge seems to couple stronger (or spread more) than it should to adjacent pads, so that the calculated centroid is pulled too much towards the peripheral pads (mostly due to saturation).
Also, there is a simple observed relationship that describes how much the centroid overestimates the actual hit position.
Example: 2 Pad hit
dx = differential nonlinearity
Actual position of hit
0mm
2mm
Nominal pad position centered on pad
Calculated centroid
1mm
Period: 0.5mm
Pitch: 2.0mm
Width: 3.0mm
q2~37.5%
Centroid(linear weighting)
0
P/4
P/2
¾ P
P
q1~62.5%
P(q1/Q) assuming linear response
Q=q1+q2
P=pitch (2mm)
Linear Centroid of two pad hit
P (1-(q1/Q))
dx
Hit Position
Note: Photo stretched and scale is not preserved

## Slide 3: Actual Hit Position Vs Centroid Calc.
Reference ~Actual hit position
(Continuous)
Calculated centroid is shifted wrt to pad edge
(Discretized around pad edge)
Centroid Calc. shifts position toward pad edge
Pad edge
Actual Position along pads
Pad edge
The centroid becomes ~discretized and pulls the calculated track position away from the actual position and toward the area between the pads in a linear way
5deg. (mostly 2Pad hits) DNL
Centroid is shifted in a systematic way toward pad edge in this case (2pad hits)
Saturation Level

## Slide 4: Magnitude of Error correction
The actual hit position here is more than 0.5mm from the pad edge (just outside the peaked centroid distribution), however, the hit position is 2*calculated centroid from the pad edge such that the residual remains less than 0.5mm.
Since DE = Dd, the calculated pos. is corrected by simply multiplying the linear centroid value by 2. Thus, the charge still couples to the pads in a linear way, but it seems the coupling process is simply enhanced by a factor of two for the peripheral pads (see next slide).
Actual hit position
Centroid
+/- 0.5mm from pad edge
Pad Edge
Centroid
Displacement
from Pad Edge: Dd
Residual:
DE
Residual is +/- 0.5mm from Pad Edge
5deg. DNL (zoomed in)
0.0
0.5
-1.0
-0.5
1.0
Actual Hit Position
Centroid
-1.0
1.0
0.0
DE
Dd
DE = Dd
0.0 = Pad Edge or
pos. btwn two pads
DE = Dd
Hit Pos. = DE + Dd = 2* Dd

## Slide 5: Interpret expression for corrected Centroid
q2~37.5%
0
P/4
P/2
¾ P
P
q1~62.5%
P(q1/Q)
C = P (1-(q1/Q))
DE
Dd
C = P(1/2 – (q1/Q))
-P/2
-P/4
0
P/4
P/2
Shift origin to P/2
DE
Dd
C’ = 2*C = P(1 – (2*q1/Q))  Same form as centroid expression above, except with origin shifted
to P/2 and charge on main pad doubled (almost like the area at P/2 is like a virtual pad)
Centroid distr. about P/2
(Nominal pad edge) for 5deg. (2Pad hits)

## Slide 6: 0 and 5 deg. data sets are good case studies
The behavior of the DNL largely depends upon the size of the charge footprint wrt to the size of the pads:
The cluster size distribution at 5 deg. mostly consists of 2 pad hits, where the centroid is peaked at the pad edges. Since the charge footprint is slightly smaller at 0 deg., the charge cluster size here consists mostly of either 1 or 2 pads hits.
Therefore, the DNL for 0deg. peaks at the center of the pads as well as at the pad edges, and must depend on the hit position in addition to the footprint size.
Since the centroid now has the freedom to equal the position between pads and the center of the pads, the error function should now have a period of 1mm and a magnitude of about 0.25mm, which it approx. does (see plot on lower right).
The residual near the pad center only extends out to 0.125mm  single pad hits are more strongly peaked than 2 pad hits and the centroid exhibits less movement
The size of the charge footprint gets steadily larger with increasing angle and one can see the evolution of the error function along the same lines as described here (see next two slides). For the larger charge footprints, corresponding to angles greater than 5deg., the fluctuations in the charge along the track leads to a large uncertainty in the centroid calculation which smears out the DNL correspondence between the hit position and the centroid (explained in more detail in later slides).
5deg.
2pad cluster
only
0deg.
1pad cluster
2pad cluster
0deg. DNL
Pad Edge Pad Center
1mm spacing
+/- 0.25mm
Pad Edge Pad Center

## Slide 7
Case study #1: 0deg.
Roughly equal number of 1 and 2 pad events
2deg.
Case study #2: 5deg.
Almost all 2 pad events
10deg.
For 0-5deg. data sets, the spread in the residual distribution is smaller than DNL error correction, therefore the error correction will have an impact on these results, but not at larger angles

## Slide 8
20deg.
30deg.
45deg.
For 20deg. there seems to be some semblance of a well defined DNL, however the width of the scatter of the residual plot (along the residual axis direction) is about the same magnitude as the DNL correction (see upper-left panel). That is the blue arrow gives an indication of the position resolution, and the red arrow gives an indication of the correction needed for the centroid calc., however there is no point to make a correction on a value that has an uncertainty associated with it at the level of the correction. Ultimately, we only have true error correction functions for 0-5 deg., corresponding to 1, 2, and 3 pad hits. (Although there are few true 3 pad hit events at 5deg., with a significant amount of charge in the tails), they are symmetric and behave more or less like 1 pad hits.
+/-1.5mm
+/-1.5mm
Scatter determines position resolution
Width determines magnitude of error due to DNL

## Slide 9: DNL for angled tracks (extended charge spread)
As the charge subtends more pads, the error on the centroid calculation gets substantially worse (as shown below), at which point the correspondence between the position of the charge along the zigzag and the offset error is smeared out and is no longer well defined.
At 0deg. the centroid error is small and the DNL is well defined, therefore one is able to successfully correct for the DNL.
At 45deg., get a broad distribution of calculated centroid values (due to large fluctuation in calculation), with no well defined DNL. As a result, applying the correction for the DNL arbitrarily worsens the resolution results.
DNL
DNL
0deg. (charge is localized around1 pad)
45deg. (Charge is extended over ~6-7pads)
Charge footprint
Centroid
For the same charge footprint, the centroid depends strongly on charge fluctuations along the track, leading to large fluctuations in the centroid for similar inclined tracks
Same charge footprint, very different centroid
Track

## Slide 10: Universal Error correction
The universal error function that we measured in the lab was correctly broken down into 2 and 3-pad hit event classes, however, I’m afraid that the hit definition may not have been sophisticated enough to distinguish between a nominal 3-pad hit, for instance, and an effective 2-pad hit. As the previous slides indicate, the behavior of the error function depends on the effective number of pads hit, and less on the actual number of pads hit. The latter quality is an incidental one, whereas the former is a substantive one. Therefore, the error function may be improved substantially if we were to make this distinction robust in the analysis.
Nominal 2 Pad Hit
Nominal 3 Pad Hit
Nominal 4 Pad Hit
Effective 2 Pad Hits
For example, although the nominal hit distribution is centered on 3 hits for 5deg., most of the events for a given charge footprint correspond to effective 2 pad hits.

## Slide 11: Compare lab (xray) residual measurements to beam test data (0deg. [1&2 pad hits])
Test beam (0deg., 1&2 pad hits)
Lab xRay (1&2 pad hits)
[must be very small in size]
It appears as though the charge footprint (or charge spread) is so small for the lab tests that the centroid is very strongly constrained to peak around the pad middle and pad edge, with little to no movement for the majority of events (vertical columns at pad edges [even mm], and dots at pad centers [odd mm]). The regions around the corresponding points along the pad structure for the beam test data results show inclined lines, an indication that the centroid has more freedom to move about these focus points, likely due to the fact that the charge footprint from the beam is larger than that from the xrays. In this case, then, the beam test data will provide a more effective error function than the lab tests will, since the error function must be charge footprint-size specific.
Different levels of charge saturation may play a role here as well in making a difference between the lab and beam test results. Although, the gain is quite similar in both cases, so saturation may be the less likely the culprit here.
Some hint of inclination
(the degree of inclination must depend on the size of the charge footprint)
ZOOM IN

## Slide 12: Continued…
There is a significant disparity in the residual Vs centroid plots (error functions) between the lab and beam test data, which is likely due to the fact that the charge footprint on the pads is significantly smaller for the lab (xray) results than for the beam test results. This implies that the lab error function is less than ideal for the beam test data and that there is a lot of potential on this front to improve the results we have so far, which use the error function measured in the lab to correct the beam test data. Ideally we need to produce an error function in a beam test, but use a different portion of the readout than is used for the resolution measurements to remain unbiased. However, using the same portion of the readout from the beam test results for both the resolution measurement and to generate an error function, though biased, certainly gives some indication of what a universal error function determined from the beam test data would look like. This was done, and the results using the beam test generated error function give noticeably better results than using the lab correction function - something like 65microns (which can be improved, I believe) Vs 85microns at zero deg. The magnitude of the correction applied by the lab error function is of the order 150microns (mostly because the prominent vertical columns average to zero when doing a Tprofile histo), but is likely two to three times this using a beam test generated error function (which has no vertical columns), implying that the latter would have a more substantial impact.

## Slide 13: Conclusions/Summary
For charge footprints much smaller than the pitch of the readout, there will be zero charge sharing and the cluster size will be strongly peaked at N=1. The centroid will then be very strongly peaked at the center of the effective pad area, and the resulting DNL will consist of a series of discrete delta functions, which makes such a chevron design not very useful. The resulting resolution will then be determined simply by the effective pad area divided by sqrt(12).
For charge footprints of the order of the size of the pad pitch, the centroid will peak at both the pad edge and pad center, however will also gain the flexibility to move away from these focus points, the larger the footprint gets . For instance, we clearly see a smaller slope (ie, movement) for the 1 pad hits (near pad center) than the 2 pad hits (near pad edge) in the error function plots on the bottom left plot of slide 11. It seems the factors that decides whether an event has an effective cluster size of 1 or two depends on both the particular size of the footprint, and on the hit position (near pad center or pad edge). For example, the 0deg. charge footprint turns into a 1 or 2 pad hit, depending on the hit position, whereas for the 5deg. footprint, just about all hit positions seem to result in two pad hits. In both cases, though, we’ve shown that the DNL error is linearly related to the displacement of the hit position from the either the center of the pad or the nominal pad edge.
For charge footprints considerably larger than the pad pitch (or effective pad area), the resulting DNL will somewhat mimic the two fundamental cases of 1pad and 2pad effective hits in that 3pad effective hits will be similar in behavior to 1pad effective hits (but 3pad hits are special since the resolution gets considerably better than a 1 pad hit), 4pad hits will be similar to 2 pad hits and so on… However, for these larger footprints, the centroid becomes very sensitive to the charge uniformity across each pad, where the resulting variation in the centroid for the same footprint can potentially grow rapidly and deteriorate the correspondence between residual and hit position (see the results for 45 deg. On side 8) Also, the magnitude of the DNL correction becomes very large. Taken together, DNL error functions for such relatively large charge footprints have little value.

## Slide 14: Continued…
For the reasons stated above, the best results are gotten when the size of the charge footprint is on par with the size of the pad readout (good/proportional charge sharing with little variation in charge uniformity) , which explains why the centroid resolution is best at small angles and poor at larger angles. Furthermore, it is likely (although it’s not proven here) that the chevron structure, enhances the requisite charge sharing while maintaining roughly the same level of charge uniformity over each pad (for charge footprints corresponding to smaller angles), compared to straight strips. The chevron structure achieves this by allowing the pad width (3mm) to be larger than the pad spacing (2mm). Perhaps it is possible to explore and optimize the corresponding level of pad overlap (0.5mm), and zigzag period (1mm) to further enhance the charge sharing to improve the resolution.
  By the way, it can be that the charge distr. for each time slice for larger angled tracks can be treated more or less independently (once the influence of the pulse tails is removed), where the resulting charge footprint at each time slice is small (similar to 0deg.) and on par with the chevron pattern.
Ultimately, the design of the chevron pattern should be driven by the size of the expected charge
footprint for each time slice, where there is significant charge sharing, and effective 1 pad hits, and
cluster sizes above ~4 hit pads should be avoided. (The reason for the latter is to avoid situations
where non-uniformities in the charge deposit heavily influence the centroid determination.)
In the present design of the BNL chevron pattern, the area of the central region is quite large so that
there is a rather large possibility for single pad hits. Together with hits near the tips of the chevron
pattern (near pad edge), makes this design a 1 and 2 pad hit type board. Ideally, the central region
(where only 1 pad occupies the area) should be kept as small as possible. This would mean moving
away from a 1&2 pad hit design, to a 2&3 pad hit design (See Alexander Kiselev’s presentation).
The vast majority of hit pads of every event for all the data sets studied here are saturated. This undoubtedly has a big impact on the results and conclusions drawn here, however, I speculate that these results at least give us an idea of how unsaturated data would behave if we had it to study. After all, 100% saturation would constrain the centroid values to equaling only discrete multiples of ½ the pad pitch, or 1mm. If this were the case, one may account for some slight variations around N*1mm due to pedestal fluctuations, however this level of variation doesn’t come close to accounting for the continuous (albeit somewhat discrete) spread in centroid values observed in the data.
1 pad hit region
2 pad hit region